.5ML v`
.c 0f
\[Directory`Formats\]

\[Standard`Floppy`Disk`(CP/M`1.4`style)\] (32 bytes)
.0c

     | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | A | B | C | D | E | F |
     |---------------------------------------------------------------|
 FCB |DSK| m*| - | - | - | - | p*| u*| r*| w*| s*| a*| - | - | - | - |
 DISK|ATT|<- - - - -FILE NAME- - - - - ->|<- -TYPE ->|EX | 0 | 0 |RC |
     |---------------------------------------------------------------|
     |                                                               |
     |<- - - - - - - - - -ALLOCATION DISK MAP- - - - - - - - - - - ->|
     |---------------------------------------------------------------|
     |10 |11 |12 |13 |14 |15 |16 |17 |18 |19 |1A |1B |1C |1D |1E |1F |

	\[ATT\]		- File attributes (on disk)
		Bits:   \[|`7```6```5```4`|`3```2```1```0`|\]
		        \[|`p```w```r```u`|`s```a```0```F'|\]

		Meanings if set (to 1)
		p: permanent		s: system file
		w: write protected	a: file has been archived
		r: read protected	0: clear bit, not used
		u: user file		F': not a file
		m: fcb modified

	*	    - Bits set in FCB by 17/18 calls or open.  These
		attributes have the same meaning as the bits of the
		same name above, and are the MSB (80H) of the bytes shown.

	\[DSK\]		- 1 Byte (in FCB)
		0	- current drive
		1..15	- drive A: through drive O:

	\[FILE`NAME\]	- 1-8, 8 characters

	\[FILE`TYPE\]	- 9-B, 3 characters
		7 bit ASCII file name right filled with spaces.

	\[EX\]		- Extent number
		Each extent uses one directory entry and can have
		16Kbytes allocated to it.

	\[RC\]		- Record Count
		Records (128 bytes each) in this extent containing
		written data. This number should be < 80H only in the
		last extent, and equal to 80H in all but the last extent.

	\[Allocation`Disk`Map\]
		Up to 16 cluster pointers, declaring up to 16K bytes
		of file, in cluster sized increments.  They are each
		one byte (1..254)
			0	- Not allocated
			255	- cluster 0 (directory)
			1..254	- cluster 1 through 254
		The first cluster is 0, the directory.