;**********************************************************
;*  							  *
;*	HDCA memory test program for onboard RAM.	  *
;*                    (BJG 1/2/83)			  *
;*							  *
;**********************************************************


          ORG  100H

BASE      EQU       50H
COMND     EQU       BASE + 1
DATA      EQU       BASE + 3
WARM      EQU       0
BDOS	  EQU	    005



; ROUTINE CHECKS FOR THE PRESENCE OF A HDCA CONTROLLER
; BOARD AT PORT 50H.

BEGIN:	  LXI  SP,1000H
          MVI  C,09H
	  LXI  D,GREET
	  CALL	BDOS
	  IN   BASE
	  CP   0FFH
	  JZ   NOBORD	
		

START:    LXI  B,512           ;SECTOR LENGTH COUNT
          LXI  H,1000H         ;MEMORY ADDRESS FOR DATA
          MVI  A,0
          OUT  COMND          ;RESET RAM POINTER TO DATA AREA
WRTLOOP:  MOV  A,M
          OUT  DATA           ;WRITE THE DATA
          INX  H
          DCX  B
          MOV A,B
          ORA C
          JNZ WRTLOOP          ;REPEAT FOR 512 BYTES
          JMP WARM
          
NOBORD: MVI	C,09H
	LXI	D,NONE
	CALL	BDOS
	JMP	AGAIN


AGAIN:  MVI	C,09
	LXI	D,NONE
	CALL	BDOS
	MVI	C,01H
	CALL	BDOS
	CMP	0DH
	JZ	BEGIN
	CMP	27
	JZ	WARM

GREET:  DB	'Morrow Designs HDCA controller RAM test'
	DB	'           Revision 0                  '
	DB	'					'
	DB	' Now testing data RAM area ...	       $ '

GREET1: DB	'					'
	DB	'Now testing header RAM area ...       $'
	
DATOK:  DB	'					'
	DB	' Data RAM area checks O.K.	       $'
	
HEDOK:  DB	'					'
	DB	' Header RAM area checks O.K.		'
	DB	' 					'
	DB	' Test concluded		      $ '
	
DATERR: DB	' 					'
	DB	' Memory failure within the DATA RAM area !! $'

HDERR:  DB	'					'
	DB	' Memory failure within the HEADER RAM area !! $'


REPEAT: DB	' If you wish to repeat this test type  '
	DB      ' a carriage return.  If you wish to exit '
	DB	' to CP/M then type the escape key...	 $'	


NONE:	DB	'There is no HDCA board present in system'
	DB      'or the board is addressed incorrectly.  To'
	DB	'address the board correctly, turn switches'
	DB	'7 and 5 on and all others off!!   $'