From Douglas Allen:

I copied and formatted this email from Steve from 1998.

Found it very interesting

My personal Altair’s serial number is 222160K

From what you see below, this means:

it is cabinet model 22

it was the 2,160th Altair made after the 5 prototypes

it was assembled from a kit.

it was manufactured between 4/2/75 and 4/24/75, but closer to the

latter.

Here is the email, but reformatted:

here is a list I acquired from various
web,newsgroup, and email requests.

steve

Model: Cardboard Mockup Altair
Number made: 1

Picture in Popular Electronics Cover Page 
This was cardboard
mock up used because.
the real Altair was built too
late to.
meet the magazine deadline for photo


Model: Prototype Altair
Number made: 5

5 prototypes were made before serial
number 1, I read about someone who has one of them

Model: 8800
Number made: 4000-5000
Serial Number: 22xxxxy
22 is part number of cabinet and power supply.
xxxx is actual serial number 0-4xxx
y = K for kit or A for assembled

Other part numbers
50 = CONT control board
10 = CPU
15 = 256 Words Memory board

Sample serial numbers and some dates of
production,
you can estimate when yours was made with this

data

22 0005 A
22 0039 K 
22 0406 K Date
2/4/75
22 0479 K
22 0864 K
22 1089 A
22 1162 K
22 1476 K 4/2/75 on warrenty card
22 1498 K
22 1639 K
22 2004 A

22 2160 K
22 2214 K
22 2217 K
22 2280 K
22 2256 K 4/24/75 invoice 
22 2504 K
22 2608 K 
22 2654 K 
22 3025 K
22 3081 K 10/75 estimate from owner
22 3087 K 
22 3543
22 3652 K

Model: 8800 Rackmount version of 8800

Used in MITS desktop, basic 8800, extended a couple
inches to fit into cabinet

Model: 8800A (type 1 silkscreen)
Number Made: 2000?
Serial Number: 22xxxxy (same as original)

Updated version of 8800, larger supply, flat switches, but
pretty much the same as 8800 

22 5948K

Model: 8800A (type 2 silkscreen)
New silkscreen, fixed power up switch

Model: 8800B 
Serial Number 54 xxxx y or 200- xxxxxxx
xxxx = serial number starting from 0000 to 0????
y = K for kit or A for assembled

Model: 8800B(T) 
Serial Number: 54 xxxxy or
300-xxxxxx

Model: 8800B-SM (T) with built in Mini Floppy (Foley)

Serial Number: 600-xxxxx