CP/M Cache file explanation		6-07-82

	The DBBIOS.ASM file now contains a new facility called Caching.
The Cache operation is used to keep the most recently used sectors in
buffers which are in extended memory, and elliminates having to re-read
the disk for those sectors again. This improves the CP/M file operations
by reducing disk access times. The most impressive improvement is seen
in random access operations.

	A couple of equates in the front of the DBBIOS.ASM file require
some explanation here.

LRU	EQU	TRUE	Causes the Cache portion to be included during
			assembly time.

NHITSC	EQU	XXX	This equate determines how many buffers are going
			to be reserved for the Cache Buffers. This equate
			can take on the values from 1 to 128 only. You can
			not set this value to 0 or greater than 128.

+--------------------------------------------------------------------------+
|                     	The value used for NHITSC directly determines the  |
| ++++  N O T E  ++++	amount of extended memory your system must have.   |
|			You must also be using memory boards which have    |
|			IEEE S-100 extended address lines. (A16 - A23)	   |
+--------------------------------------------------------------------------+

Example:	If you have 64 K of extended memory (128K total), you could
		set NHITSC = 128. This means that as far as CP/M is concerned,
		you have 512 CP/M record buffers in memory.

		If you have 32 K of extended memory (96K total), you could
		set NHITSC = 64. This means that as far as CP/M is concerned,
		you have 256 CP/M record buffers in memory

		To compute how much memory is needed for the value of NHITSC
		chosen, use the following equation.

			EXT_MEM size = (NHITSC / 8) * 4096

MSIZE	EQU	XX	If you use the Caching function, the largest your CP/M
			system can be is 62K.

			Known Problems
			--------------

PIP			You can not PIP a file from Drive A to Drive B if
			the disk you are piping from was not the disk you
			brought the system up on. The directory that is in
			the Cache Buffers is from the System disk directory.

			To avoid this problem, transfer the file first to
			Drive A from the B drive, then place the disk you
			wanted the file to go to into the B drive and do
			a warmboot. Then transfer the file to the B Drive
			from the A Drive. In other words, you will need to
			do a double transfer.

NOTE:  This system works only with disks that are formatted double denisty,
       512 bytes per sector, single or double sided.  Use the normal deblock
       BIOS with LRU set to FALSE in order to transfer files to the 512 byte
       disks from disks formatted other ways.