Documentation on new features of CCPZ vers 2.7
	----------------------------------------------

  CCPZ version 2.7 is completely compatible with the preceding version 2.6,
but contains an additional command (GO), an alternate method of setting
the CCPLOC equate value with two new symbols (MSIZE and BIOSEX), and an
additional customization equate (FENCE).

  To provide additional space for implementing the GO command, some
furthur jump optimization was performed in various places in the code.

  In addition, changes were made to the Z80 branch macros for esthetic
reasons and to provide more information if a "branch out of range"
error occurred. Specifically, a V(alue) error was forced to get MAC
to print out the current location counter value to help locate the
exact jump that was out of range.

  The release CCP and CCPZ version 2.6 do not reset the default DMA
address after calling a program in the TPA (or elsewhere for CCPZ).
As a result, if the called program changes the DMA address, and CCP
is in a SUBMIT run, the next read on the SUBMIT file will NOT go
into the default buffer as desired, but SOMEWHERE ELSE! Funny cases
surrounding the use of STAT in a SUBMIT run can usually be traced
to this bug. CCPZ version 2.7 has this problem corrected.


			New GO command
			--------------

  CCPZ version 2.6 supports a JUMP command which has the capability
of "calling" a program anywhere in memory. Certain serially re-entrant
programs like STAT can be "used again" after having been run once
by issuing the command "JUMP 100 <parameters>", where <parameters>
are legitimate input on the command line to be passed to STAT. This
command has the same effect as issuing the command "STAT <parameters>",
without loading a new copy of STAT from the disk. Many popular directory
programs also may be used in this way. Using the above form of the
JUMP command may be recognizable to users of the old IMSAI IMDOS
system, as it is equivalent to the IMDOS "GO" command. However,
as described in the program source and implementation notes, the
potentially-disastrous JUMP command may be undesirable for remote
CP/M system usage, and can be disabled with the RAS option. It is
for this reason and for convenience that CCPZ version 2.7 contains
an IMDOS-style "GO <parameters>" command, exactly equivalent to
the "JUMP 100 <parameters>" command described above, but not subject
to being disabled by the RAS option, since there is no reason to
do so.


		Alternate CCPLOC value determination
		------------------------------------

  The implementation notes describe how an earlier version of CCPZ
contained system parameters for determining the value of CCPLOC, and
that these were deleted along the way in favor of just using a
program called BDOSLOC to determine the current location of the
user's CCP. This value could then be used as the value of the CCPLOC
symbol.

  That is fine for the committee that came up with that decision.
The implementer of the version 2.7 changes feels that while that
may be adequate for them, others desire the documentation inherent
in relating CCPLOC to actual system parameters. The source now
contains the following to allow either method to be used:

    ;
    ;  If REL is FALSE, the value of CCPLOC may be set in one
    ; of two ways. The first way is to set MSIZE and BIOSEX
    ; as described above, using the following three lines:
    ;
    MSIZE   EQU     56	    ;SIZE OF MEM IN K-BYTES
    BIOSEX  EQU     1	    ;EXTRA # K-BYTES IN BIOS
    CCPLOC  EQU     3400H+(MSIZE-20-BIOSEX)*1024 ;CCP ORIGIN
    ;
    ;  The second way is to obtain the origin of your current
    ; CCP using BDOSLOC or its equivalent, then merely set CCPLOC
    ; to that value, as in the following line:
    ;
    ;CCPLOC EQU     0C000H  ;FILL IN WITH BDOSLOC-SUPPLIED VALUE
    ;
    ;  Note that you should only use one method or the other.
    ; Do NOT define CCPLOC TWICE!
    ;

  Either CCPLOC equate will define the origin of CCPZ in a
56K system where the BIOS is 1K larger than the standard
Digital Research release BIOS. Note that a semi-colon was
placed in front of the second CCPLOC equate line, which was
unused. By deleting the semi-colon, and setting the value
to that supplied by BDOSLOC, that line would be valid, and
the first CCPLOC equate line should then have a semi-colon
inserted at its front instead.


	   Directory file name separater (FENCE)
	   -------------------------------------

  For those people who prefer another character to the colon
that was used to separate file names on the DIR and ERA
reports, the FENCE symbol may be equated to the character
of their choice. A popular alternative is the vertical bar ("|")
symbol, and is in fact the value of FENCE in CCPZ version 2.7.
For those who disagree with that choice, FENCE may be set
to the colon or any other character. Colon and vertical bar
are the usual choices.