Z-80 Macro Library Documentation
		--------------------------------

I.
	The purpose of this library is to enable the assembly of the Z-80
    instruction set on a CP/M sytem using the CP/M MAC macro assembler.

	This library is invoked with the pseudo-op:

		"  MACLIB  Z80	"

II.
	The following symbols and notations are used in the individual macro
    descriptions;

	r - Any of the 8 bit registers: A, B, C, D, E, H, L, or M
	rr - Any of the 16 bit register pairs: BC, DE, HL, or SP
	nn - 8 bit immediate data (0 through 255)
	d  - 8 bit signed displacment (-128 through +127)
	nnnn - 16 bit address or immediate data (0 through 65535)
	b  - bit number (0-7, 7 is most significant, 0 is least)
	addr - 16 bit address within PC+127 through PC-128
	m(zzz) - Memory at address "zzz"

III.

 MACLIB ver.		  Zilog ver		   TDL ver
--------------		-------------		-------------

LDX	r,d		LD	r,(IX+d)	MOV	r,d(IX)
    Load register from indexed memory (with IX)

LDY	r,d		LD	r,(IY+d)	MOV	r,d(IY)
    Load register from indexed memory (with IY)

STX	r,d		LD	(IX+d),r	MOV	d(IX),r
    Store register to indexed memory (with IX)

STY	r,d		LD	(IY+d),r	MOV	d(IY),r
    Store register to indexed memory (with IY)

MVIX	nn,d		LD	(IX+d),nn	MVI	d(IX)
    Move immediate to indexed memory (with IX)

MVIY	nn,d		LD	(IY+d),nn	MVI	d(IY)
    Move immediate to indexed memory (with IY)

LDAI			LD	A,I		LDAI
    Move I to A

LDAR			LD	A,R		LDAR
    Move R to A

STAI			LD	I,A		STAI
    Move A to I

STAR			LD	R,A		STAR
    Move A to R

LXIX	nnnn		LD	IX,nnnn 	LXI	IX,nnnn
    Load IX immediate (16 bits)

LXIY	nnnn		LD	IY,nnnn 	LXI	IY,nnnn
    Load IY immediate (16 bits)

LBCD	nnnn		LD	BC,(nnnn)	LBCD	nnnn
    Load BC direct (from memory at nnnn)

LDED	nnnn		LD	DE,(nnnn)	LDED	nnnn
    Load DE direct

LSPD	nnnn		LD	SP,(nnnn)	LSPD	nnnn
    Load SP direct

LIXD	nnnn		LD	IX,(nnnn)	LIXD	nnnn
    Load IX direct

LIYD	nnnn		LD	IY,(nnnn)	LIYD	nnnn
    Load IY direct

SBCD	nnnn		LD	(nnnn),BC	SBCD	nnnn
    Store BC direct (to memory at nnnn)

SDED	nnnn		LD	(nnnn),DE	SDED	nnnn
    Store DE direct

SSPD	nnnn		LD	(nnnn),SP	SSPD	nnnn
    Store SP direct

SIXD	nnnn		LD	(nnnn),IX	SIXD	nnnn
    Store IX direct

SIYD	nnnn		LD	(nnnn),IY	SIYD	nnnn
    Store IY direct

SPIX			LD	SP,IX		SPIX
    Copy IX to the SP

SPIY			LD	SP,IY		SPIY
    Copy IY to the SP

PUSHIX			PUSH	IX		PUSH	IX
    Push IX into the stack

PUSHIY			PUSH	IY		PUSH	IY
    Push IY into the stack

POPIX			POP	IX		POP	IX
    Pop IX from the stack

POPIY			POP	IY		POP	IY
    Pop IY from the stack

EXAF			EX	AF,AF'		EXAF
    Exchange AF and the alternate, AF'

EXX			EXX			EXX
    Exchange BC DE HL with BC' DE' HL'

XTIX			EX	(SP),IX 	XTIX
    Exchange IX with the top of the stack

XTIY			EX	(SP),IY 	XTIY
    Exchange IY with the top of the stack

LDI			LDI			LDI
    Move m(HL) to m(DE), increment DE and HL, decrement BC

LDIR			LDIR			LDIR
    Repeat LDI until BC = 0

LDD			LDD			LDD
    Move m(HL) to m(DE), decrement HL, DE, and BC

LDDR			LDDR			LDDR
    Repeat LDD until BC = 0

CCI			CPI			CCI
    Compare A with m(HL), increment HL, decrement BC

CCIR			CPIR			CCIR
    Repeat CCI until BC = 0  or  A = m(HL)

CCD			CPD			CCD
    Compare A with m(HL), decrement HL and BC

CCDR			CPDR			CCDR
    Repeat CCD until BC = 0 or A = m(HL)

ADDX	d		ADD	(IX+d)		ADD	d(IX)
    Indexed add to A

ADDY	d		ADD	(IY+d)		ADD	d(IY)
    Indexed add to A

ADCX	d		ADC	(IX+d)		ADC	d(IX)
    Indexed add with carry

ADCY	d		ADC	(IY+d)		ADC	d(IY)
    Indexed add with carry

SUBX	d		SUB	(IX+d)		SUB	d(IX)
    Indexed subtract

SUBY	d		SUB	(IY+d)		SUB	d(IY)
    Indexed Subtract

SBCX	d		SBC	(IX+d)		SBB	d(IX)
    Indexed subtract with "borrow"

SBCY	d		SBC	(IY+d)		SBB	d(IY)
    Indexed subtract with borrow

ANDX	d		AND	(IX+d)		ANA	d(IX)
    Indexed logical and

ANDY	d		AND	(IY+d)		ANA	d(IY)
    Indexed logical and

XORX	d		XOR	(IX+d)		XRA	d(IX)
    Indexed logical exclusive or

XORY	d		XOR	(IY+d)		XRA	d(IY)
    Indexed logical exclusive or

ORX	d		OR	(IX+d)		ORA	d(IX)
    Indexed logical or

ORY	d		OR	(IY+d)		ORA	d(IY)
    Indexed logical exclusive or

CMPX	d		CP	(IX+d)		CMP	d(IX)
    Indexed compare

CMPY	d		CP	(IY+d)		CMP	d(IY)
    Index compare

INRX	d		INC	(IX+d)		INR	d(IX)
    Increment memory at m(IX+d)

INRY	d		INC	(IY+d)		INR	d(IY)
    Increment memory at m(IY+d)

DCRX	d		INC	(IX+d)		INR	d(IX)
    Decrement memory at m(IX+d)

DCRY	d		DEC	(IY+d)		DCR	d(IY)
    Decrement memory at m(IX+d)

NEG			NEG			NEG
    Negate A (two's complement)

IM0			IM0			IM0
    Set interrupt mode 0

IM1			IM1			IM1
    Set interrupt mode 1

IM2			IM2			IM2
    Set interrupt mode 2

DADC	rr		ADC	HL,rr		DADC	rr
    Add with carry rr to HL

DSBC	rr		SBC	HL,rr		DSBC   rr
    Subtract with "borrow" rr from HL

DADX	rr		ADD	IX,rr		DADX	rr
    Add rr to IX (rr may be BC, DE, SP, IX)

DADY	rr		ADD	IY,rr		DADY   rr
    Add rr to IY (rr may be BC, DE, SP, IY)

INXIX			INC	IX		INX	IX
    Increment IX

INXIY			INC	IY		INX	IY
    Increment IY

DCXIX			DEC	IX		DCX	IX
    Decrement IX

DCXIY			DEC	IY		DCX	IY
    Decrement IY

BIT	b,r		BIT	b,r		BIT	b,r
    Test bit b in register r

SETB	b,r		SET	b,r		SET	b,r
    Set bit b in register r

RES	b,r		RES	b,r		RES	b,r
    Reset bit b in register r

BITX	b,d		BIT	b,(IX+d)	BIT	b,d(IX)
    Test bit b in memory at m(IX+d)

BITY	b,d		BIT	b,(IY+d)	BIT	b,d(IY)
    Test bit b in memory at m(IY+d)

SETX	b,d		SET	b,(IX+d)	SET	b,d(IX)
    Set bit b in memory at m(IX+d)

SETY	b,d		SET	b,(IY+d)	SET	b,d(IY)
    Set bit b in memory at m(IY+d)

RESX	b,d		RES	b,(IX+d)	RES	b,d(IX)
    Reset bit b in memory at m(IX+d)

RESY	b,d		RES	b,(IY+d)	RES	b,d(IY)
    Reset bit b in memory at m(IY+d)

JR	addr		JR	addr-$		JMPR	addr
    Jump relative unconditional

JRC	addr		JR	C,addr-$	JRC	addr
    Jump relative if Carry indicator true

JRNC	addr		JR	NC,addr-$	JRNC	addr
    Jump relative if carry indicator false

JRZ	addr		JR	Z,addr-$	JRC	addr
    Jump relative if Zero indicator true

JRNZ	addr		JR	NZ,addr-$	JRNZ	addr
    Jump relative if Zero indicator false

DJNZ	addr		DJNZ	addr-$		DJNZ	addr
    Decrement B, jump relative if non-zero

PCIX			JMP	(IX)		PCIX
    Jump to address in IX ie, Load PC from IX

PCIY			JMP	(IY)		PCIY
    Jump to address in IY

RETI			RETI			RETI
    Return from interrupt

RETN			RETN			RETN
    Return from non-maskable interrupt

INP	r		IN	r,(C)		INP	r
    Input from port C to register r

OUTP	r		OUT	(C),r		OUTP	r
    Output from register r to port (C)

INI			INI			INI
    Input from port (C) to m(HL), increment HL, decrement b

INIR			INIR			INIR
    Input from port (C) to m(HL), increment HL, decrement B, repeat if B <> 0

OUTI			OTI			OUTI
    Output from m(HL) to port (C), increment HL, decrement B

OUTIR			OTIR			OUTIR
    Repeat OUTI until B = 0

IND			IND			IND
    Input from port (C) to m(HL), decrement HL & B

INDR			INDR			INDR
    Repeat IND until B = 0

OUTD			OTD			OUTD
    Output from m(HL) to port (C), decrement HL & B

OUTDR			OTDR			OUTDR
    Repeat OUTD until B = 0

RLCR	r		RLC	r		RLCR	r
    Rotate left circular register

RLCX	d		RLC	(IX+d)		RLCR	d(IX)
    Rotate left circular indexed memory

RLCY	d		RLC	(IY+d)		RLCR	d(IY)
    Rotate left circular indexed memory

RALR	r		RL	r		RALR	r
    Rotate left arithmetic register

RALX	d		RL	(IX+d)		RALR	d(IX)
    Rotate left arithmetic indexed memory

RALY	d		RL	(IY+d)		RALR	d(IY)
    Rotate left arithmetic indexed memory

RRCR	r		RRC	r		RRCR	r
    Rotate right circular register

RRCX	d		RRC	(IX+d)		RRCR	d(IX)
    Rotate right circular indexed

RRCY   d	       RRC     (IY+d)	       RRCR    d(IY)
    Rotate right circular indexed

RARR	r		RR	r		RARR	r
    Rotate right arithmetic register

RARX	d		RR	(IX+d)		RARR	d(IX)
    Rotate right arithmetic indexed memory

RARY	d		RR	(IY+d)		RARR	d(IY)
    Rotate right arithmetic indexed memory

SLAR	r		SLA	r		SLAR	r
    Shift left register

SLAX	d		SLA	(IX+d)		SLAR	d(IX)
    Shift left indexed memory

SLAY	d		SLA	(IY+d)		SLAR	d(IY)
    Shift left indexed memory

SRAR	r		SRA	r		SRAR	r
    Shift right arithmetic register

SRAX	d		SRA	(IX+d)		SRAR	d(IX)
    Shift right arithmetic indexed memory

SRAY	d		SRA	(IY+d)		SRAR	d(IY)
    Shift right arithmetic indexed memory

SRLR	r		SRL	r		SRLR	r
    Shift right logical register

SRLX	d		SRL	(IX+d)		SRLR	d(IX)
    Shift right logical indexed memory

SRLY	d		SRL	(IY+d)		SRLR	d(IY)
    Shift right logical indexed memory

RLD			RLD			RLD
    Rotate left digit

RRD			RRD			RRD
    Rotate right digit